## Slide 1: Making a Batch Manually
6.25.24 version 1.0

## Slide 2
Assumptions and Prerequisite Skills
  The computer is on and IntelliBatch 3.0 is open
Supplies Needed
  Standard PPE

## Slide 3: Preface
This procedure focuses on making one batch at a time. If for any reason you would need to manually make multiple batches quickly you should use the pipelining technique which is how batches are made when all settings are set to “auto”. Pipelining is when all stations are working simultaneously so that once one station finishes up its work required on a batch, that same station can start working on the next batch immediately.

## Slide 4
1. Click on the “Manual” text on the “Scaling 1” switch (Figure 1).
Figure 1

## Slide 5
2. Click the orange triangle on one of the first four aggregate bins (Red circle in Figure 2).
Figure 2

## Slide 6
3. Click on the run button until the Aggregate Weighbelt has reached about 5000 lbs. (Blue circle in Figure 3). While doing this, switch back and forth between the two gates so that neither gate gets clogged.
4. Click on the jog button (Red circle in Figure 3) until the Weighbelt has reached 5200 lbs.
Figure 3

## Slide 7
Click on the orange triangle on the “Flexwall belt” icon.
Click the “Run” button under the forward tab (Blue circle in Figure 4).
Figure 4

## Slide 8
7. Click on the orange triangle on the “Aggregate Weighbelt” icon.
8. Click the “Run” button under the forward tab (Blue circle in Figure 5).
Figure 5

## Slide 9
9. Click on the orange triangle on one of the Cement Silos.
10. Click the “Run” button until The cement scale reaches about 640 lbs. (Blue circle in Figure 6).
11. Click and hold the “jog” button until the cement scale reaches 650 lbs. (Purple circle in Figure 6).
Figure 6

## Slide 10
12. Click on the “Manual” text on the “Mixing 1” switch (Figure 7).
Figure 7

## Slide 11
13. Click on the “Agg Holding Hopper” and click “open” (Purple circle in Figure 8a).
14. Wait until the “Aggregate Weighbelt” value is 0 (or close to 0 for a long period of time). Once this happens, click the “Close” button (Purple circle in Figure 8b).
Figure 8a
Figure 8b

## Slide 12
15. Click on the cement scale and click “open” (Purple circle in Figure 9).
16. Wait until the “Cement Scale” value is 0 (or close to it for a long period of time). Once this happens, click the “Close” button.
Figure 9

## Slide 13
17. Click on the “Master Glenium 7620” icon and press and hold on the “Charge to Mixer” button for 5 seconds (Green circle in Figure 10).
Figure 10

## Slide 14
18. Click on the “fast” button on the water table and hold the button until the probe is about .2% from the discharge moisture of the last batch (Red circle in Figure 11).
Figure 11

## Slide 15
19. Click on the “slow” button on the water table and hold the button until the probe reaches the discharge moisture of the last batch (Red circle in Figure 12).
Figure 12

## Slide 16
20. Click on the “Manual” text on the “Discharging 1” switch (Figure 13).
Figure 13

## Slide 17
21. Click on the “Manual” text on the “Discharging” switch.
Click on the orange triangle on the Mixer icon. Press and hold the “open” button under “Mud Hopper 2” until the light next to the “open” label lights up (Blue circle in Figure 14).
22. Watch the “Mud Hopper 2” weight value. Once you see the value no longer going up, press and hold the “close” button under “Mud Hopper 2” until the light next to the “close” label lights up (Purple Circle in Figure 14).
Figure 14

## Slide 18
23. Click on the orange triangle under the “Machine Belt” icon. Click the “Run” button under the forward tab (Blue circle in Figure 15).
Figure 15

## Slide 19
24. Click on the orange triangle under the “Mud Hopper 2” icon. Click the “Run” button under the forward tab. Your screen should look like Figure 16.
Figure 16

## Slide 20
25. Watch the Feed Belt hopper and make sure the “MTL Hopper” value is not over 800 (orange circle in Figure 17). Once the value hits 700, Stop both the machine belt and Mud Hopper belts until the hopper is close to empty again.
26. Repeat steps 22-23 until the batch has gone through the block machine.
Figure 17