## Slide 1: Product Changeover (Wet Side)
7.25.24 version 2.0

## Slide 2
Assumptions and Prerequisite Skills
  The unloading bay has current unloading product stuck behind loading product
  Requires strong knowledge of how the Bessermatic works, as well as the curing process of racks regarding loading and unloading from the car
Supplies Needed
  Standard PPE

## Slide 3
1. Outside the control room, there is a chart indicating what product is in each bay. If a bay has a combination of two or more different products (ex: “2 racks 8x16, 2 racks 10x16”), there is a chance the unloading product is stuck behind the loading product.
Figure 1

## Slide 4
2. Before the car goes to that bay, proceed to the control panel next to the kiln door. Flip the control switch to the “manual” position.
3. Turn and hold the “Kiln Door” switch to the “open” position until the door is no longer moving. Be mindful to slow the door down when nearing the back-stop to prevent slamming.
Figure 2

## Slide 5
4. Go to the bay with the mixed products and assess how many racks have the unloading product. Keep in mind that there may be a rack that has both loading and unloading product. This needs to be taken into consideration.

## Slide 6: Possible Scenarios
1
2
3
4
5
6
7
Loading Product
Unloading Product
Mixed Rack (some loading some unloading)

## Slide 7: Scenario #1 & #2
  1.1. Wait until the crawler has loaded rack 4 onto the new loading bay and has just retrieved its unloading rack. Flip the car control switch to the “Hand” position (Green circle in Figure 1.2).
Figure 1.2
Figure 1.1
Unloading Bay
Loading Bay
Rack 1
Mixed
Rack 2
Loading
Rack 3
Loading
Rack 4
Loading
Rack 1
Loading

## Slide 8
  1.2. Use the lever on the second row to move the car to the “reverse” position (Red circle in Figure 1.3). You can press the “Manual Accel” button to speed the car up (Pink circle in Figure 1.3).
Scenario #1 & #2
Figure 1.3

## Slide 9: Scenario #1 & #2
  1.3. hold the “Reverse” lever from step 1.2 until the “Car Centered Left” button lights up (Figure 1.4).
Figure 1.4 : off
Figure 1.4: on

## Slide 10: Scenario #1 & #2
    1.4. Flip the “Left Raillocks” switch to the “Lock” position (Purple arrow in Figure 1.5) and hold it at that position until you see the “Left Locks Locked” box (Figure 1.6).
Figure 1.5
Figure 1.6. unlocked
Figure 1.6: locked

## Slide 11: Scenario #1 & #2
    1.5. Figure 1.7 is what the loading bay should now look like.
Unloading Bay
Loading Bay
Figure 1.7
Car
Rack 1
Mixed
Rack 2
Loading
Rack 3
Loading
Rack 1
Loading
Rack 4
Loading

## Slide 12: Scenario #1 & #2
    1.6. Once the crawler comes back to the car, unlock the raillocks (Purple circle in Figure 1.8), and move the car forward back to the unloading bay. Lock the left raillocks again, making the crawler unload the next rack.
Figure 1.8

## Slide 13: Scenario #1 & #2
    1.7. Repeat 1.1-1.6 until the Loading and Unloading bay looks like Figure 1.9. You now have access to the mixed rack.
Unloading Bay
Loading Bay
Figure 1.9
Rack 1
Mixed
Rack 1
Loading
Rack 4
Loading
Rack 3
Loading
Rack 2
Loading
Car

## Slide 14: Scenario #1 & #2
    1.8. Move the car forward once more collecting the rack with the mixed product. Lock the left raillocks.

## Slide 15: Scenario #1 & #2
    1.9. While the crawler is collecting the final rack, go to the “Program Car” page (Red circle in Figure 1.10).
Figure 1.10

## Slide 16: Scenario #1 & #2
    1.10. Press on the blue box to the right of the “Location” label until the box says “Car at Storage” (Yellow circle in Figure 1.11). “Car at Storage” indicates that the car is unloading a rack from a bay to be transferred to the unloading side of the Bessermatic.
Figure 1.11

## Slide 17: Scenario #1 & #2
    1.11. Flip the Control switch back to the “Auto” position. Hit the “Pump Auto Start” button (Purple circle in Figure 1.12).
Figure 1.12

## Slide 18: Scenario #1 & #2
1.11. Go to the kiln door control panel. Flip the control switch to “Auto” and press the “Auto Start” button (Red circle in Figure 1.13).
Figure 1.13

## Slide 19: Scenario #3
    3.1. Wait until the crawler has loaded its first rack onto the new loading bay and has just retrieved its unloading rack (Figure 3.1). Flip the car control switch to the “Hand” position (Green circle in Figure 3.2).
Figure 3.2
Unloading Bay
Loading Bay
Figure 3.1
Rack 1
Unloading
Rack 2
Mixed
Rack 3
Loading
Rack 4
Loading
Rack 1
Loading
Car

## Slide 20: Scenario #3
    3.2. Use the lever on the second row to move the car to the “reverse” position (Red circle in Figure 3.3). You can press the “Manual Accel” button (Pink circle in Figure 3.3) to speed the car up.
Figure 3.3

## Slide 21: Scenario #3
    3.3. hold the “Reverse” lever from step 3.2 until the “Car Centered Left” button lights up (Figure 3.4).
Figure 3.4: off
Figure 3.4: on

## Slide 22: Scenario #3
    3.4. Flip the “Left Raillocks” switch to the “Lock” position (purple arrow in Figure 3.5) and hold it at that position until you see the “Left Locks Locked” box (red circles in Figure 3.6).
Figure 3.6: Locked
Figure 3.6: Unlocked
Figure 3.5

## Slide 23: Scenario #3
    3.5. Figure 3.7 is what the loading bay should now look like.
Loading Bay
Unloading Bay
Figure 3.7
Rack 1
Unloading
Rack 2
Mixed
Rack 3
Loading
Rack 1
Loading
Rack 4
Loading
Car

## Slide 24: Scenario #3
    3.6. Once the crawler comes back to the car, unlock the raillocks (purple circle in Figure 3.8), and move the car forward back to the unloading bay. Lock the left raillocks again, making the crawler unload the next rack.
Figure 3.8

## Slide 25: Scenario #3
    3.7. Repeat 3.1-3.6 until the Loading and Unloading bay looks like Figure 3.9.
Figure 3.9
Unloading Bay
Rack 1
Unloading
Rack 2
Mixed
Loading Bay
Rack 1
Loading
Rack 4
Loading
Rack 3
Loading
Car

## Slide 26: Scenario #3
    3.8. Move the car forward once more collecting the rack with the mixed product. Lock the left raillocks.
Figure 3.10
Unloading Bay
Rack 1
Unloading
Rack 2
Mixed
Loading Bay
Rack 1
Loading
Rack 4
Loading
Rack 3
Loading
Car

## Slide 27: Scenario #3
    3.9. Once the crawler collects this rack and safely returns to the car, move the car out of the kiln room to the auxiliary railway (Red circle in Figure 3.11).
Unloader
Loader
Kiln Room
Figure 3.11
Bessermatic (Loading)
Bessermatic (Unloading)
Auxiliary

## Slide 28: Scenario #3
    3.10. Before you unlock the rail, flip the “Manual Crawler Auto” switch to the “Crawler” position (red circle in Figure 3.12).
Figure 3.12

## Slide 29: Scenario #3
    3.11. Instead of locking the left raillocks, you would want to lock the right raillocks this time (Purple arrow in Figure 3.13).
Figure 3.13

## Slide 30: Scenario #3
    3.12. At this time, move and hold the “Crawler” lever to the “Right” position (Red circle in Figure 3.14) until the entire rack is on the storage railway.
Figure 3.14

## Slide 31: Scenario #3
    3.13. Move and hold the “Crawler Elevator” lever to the “Down” position (Red circle in Figure 3.15) until the rack is independently sitting on the rail.
Figure 3.15

## Slide 32: Scenario #3
    3.14. Move the crawler back into the car. Hold the lever until you see the “Crawler on Car” label light up (Red circles in Figure 3.16).
Figure 3.16: Crawler Off Car
Figure 3.16: Crawler On Car

## Slide 33: Scenario #3
    3.15. Move the car back into the kiln room to pick up the fully unloading rack.
Unloading Bay
Loading Bay
Figure 3.17
Rack 1
Loading
Rack 4
Loading
Rack 3
Loading
Rack 1
Unloading
Car

## Slide 34: Scenario #3
    3.16. Move this rack out of the kiln room but this time, drop it off on the loading rail (Red circle in Figure 3.18). No need to manually move the crawler this time.
Figure 3.18
Unloader
Loader
Kiln Room
Rack 2
Mixed
Rack 1
Unloading
New Loading Rack
Bessermatic (Loading)
Bessermatic (Unloading)
Car
Auxiliary

## Slide 35: Scenario #3
    3.17. To reduce down-time, collect the loading product and put it in the same bay where all the other loading products have been placed.
Unloader
Loader
Kiln Room
Figure 3.19
Rack 2
Mixed
Bessermatic (Loading)
Bessermatic (Unloading)
New Loading Rack
Car
Auxiliary

## Slide 36: Scenario #3
3.18. Once that rack has been dropped off, move the car out of the kiln room, pick up the mixed rack from the auxillary rail, and place it on the Unloading rail.
Bessermatic (Loading)
Bessermatic (Unloading)
Unloader
Loader
Kiln Room
Figure 3.20
Rack 2
Mixed
Car
Auxiliary

## Slide 37: Scenario #3
    3.19. While the crawler is dropping off the final rack, go to the “Program Car” page (Red circle in Figure 3.21).
Figure 3.21

## Slide 38: Scenario #3
    3.20. Press on the blue box to the right of the “Location” label until the box says, “Car at Loader” (Yellow circle in Figure 3.22).
Figure 3.22

## Slide 39: Scenario #3
3.21. Flip the control switch back to “Auto” and press the “Auto Pump Start” button (Purple circle in Figure 3.23).
Figure 3.23

## Slide 40: Scenario #4
4.1. Wait until the crawler has loaded its first rack onto the new loading bay and has just retrieved its unloading rack. Flip the car control switch to the “Hand” position (Green circle in Figure 4.2).
Figure 4.2
Loading Bay
Figure 4.1
Unloading Bay
Rack 1
Unloading
Rack 2
Unloading
Rack 3
Loading
Rack 4
Loading
Rack 1
Loading

## Slide 41: Scenario #4
4.2. Use the lever on the second row to move the car to the “reverse” position (Red circle in Figure 4.3). You can press the “Manual Accel” button to speed the car up (Pink circle in Figure 4.3).
Figure 4.3

## Slide 42: Scenario #4
4.3. hold the “Reverse” lever from step 1.2 until the “Car Centered Left” button lights up (Figure 4.4).
Figure 4.4: off
Figure 4.4: on

## Slide 43: Scenario #4
4.4. Flip the “Left Raillocks” switch to the “Lock” position (Purple arrow in Figure 4.5) and hold it at that position until you see the “Left Locks Locked” box (Red circles in Figure 4.6).
Figure 4. 6: Crawler Off Car
Figure 4.6: Crawler On Car
Figure 4.5

## Slide 44: Scenario #4
4.5. Figure 4.7 is what the loading bay should now look like.
Figure 4.7
Unloading Bay
Rack 1
Unloading
Rack 2
Unloading
Rack 3
Loading
Loading Bay
Rack 4
Loading
Rack 1
Loading

## Slide 45: Scenario #4
4.6. Once the crawler comes back to the car, unlock the raillocks (Purple arrow in Figure 4.8), and move the car forward back to the unloading bay. Lock the left raillocks again, making the crawler unload the next rack.
Figure 4.8

## Slide 46: Scenario #4
4.7. Repeat 4.1-4.6 until the Loading and Unloading bay looks like Figure 4.9.
Figure 4.9
Unloading Bay
Rack 1
Unloading
Rack 2
Unloading
Loading Bay
Rack 3
Loading
Rack 4
Loading
Rack 1
Loading

## Slide 47: Scenario #4
4.8. Move the car forward once more collecting the rack with the mixed product. Lock the left raillocks.
Unloading Bay
Rack 1
Unloading
Rack 2
Unloading
Loading Bay
Figure 4.10
Rack 3
Loading
Rack 4
Loading
Rack 1
Loading

## Slide 48: Scenario #3
    4.9. While the crawler is dropping off the final rack, go to the “Program Car” page (Red circle in Figure 4.11).
Figure 4.11

## Slide 49: Scenario #3
    4.10. Press on the blue box to the right of the “Location” label until the box says, “Car at Loader” (Yellow circle in Figure 4.12).
Figure 4.12

## Slide 50: Scenario #4
4.11. Flip the Control switch back to the “Auto” position. Hit the “Pump Auto Start” button (Purple circle in Figure 4.13).
Figure 4.13

## Slide 51: Scenario #5
    5.1. Wait until the crawler has loaded its first rack onto the new loading bay and has just retrieved its unloading rack. Flip the car control switch to the “Hand” position (Green circle in Figure 5.2).
Figure 5.2
Loading Bay
Rack 1
Loading
Unloading Bay
Figure 5.1
Rack 1
Unloading
Rack 2
Unloading
Rack 3
Mixed
Rack 4
Loading

## Slide 52: Scenario #5
    5.2. Use the lever on the second row to move the car to the “reverse” position (Red circle in Figure 5.3). You can press the “Manual Accel” button (Pink circle in Figure 5.3) to speed the car up.
Figure 5.3

## Slide 53: Scenario #5
    5.3. hold the “Reverse” lever from step 1.2 until the “Car Centered Left” button lights up (Figure 5.4).
Figure 5.4: off
Figure 5.4: on

## Slide 54: Scenario #5
    5.4. Flip the “Left Raillocks” switch to the “Lock” position (Purple arrow in Figure 5.5) and hold it at that position until you see the “Left Locks Locked” box (Red circles in Figure 5.6).
Figure 5.6: Crawler Off Car
Figure 5.6: Crawler On Car
Figure 5.5

## Slide 55: Scenario #5
    5.5. Figure 5.7 is what the loading bay should now look like.
Unloading Bay
Rack 1
Unloading
Rack 2
Unloading
Rack 3
Mixed
Loading Bay
Figure 5.7
Rack 1
Loading
Rack 4
Loading

## Slide 56: Scenario #5
    5.6. Once the crawler comes back to the car, unlock the raillocks, and move the car forward back to the unloading bay. Lock the left raillocks again (Purple arrow in Figure 5.8), making the crawler unload the next rack.
Figure 5.8

## Slide 57: Scenario #5
    5.7. Once the crawler collects this rack and safely returns to the car, move the car out of the kiln room to the auxillary railway from the door (Red circle in Figure 5.9).
Unloader
Loader
Kiln Room
Figure 5.9
Bessermatic (Loading)
Bessermatic (Unloading)
Auxiliary

## Slide 58: Scenario #5
    5.8. Before you unlock the rail, flip the “Manual Crawler Auto” switch to the “Crawler” position (Red circle in Figure 5.10).
Figure 5.10

## Slide 59: Scenario #5
    5.9. Instead of locking the left raillocks, you would want to lock the right raillocks this time (Purple circle in Figure 5.11).
    Please be careful in ensuring you are locking the correct side as this can result in the crawler derailing off the car.
Figure 5.11

## Slide 60: Scenario #5
    5.10. At this time, move and hold the “Crawler” lever to the “Right” position (Red circle in Figure 5.12) until the entire rack is on the storage railway.
Figure 5.12

## Slide 61: Scenario #5
    5.11. Move and hold the “Crawler Elevator” lever to the “Down” position (Red circle in Figure 5.13) until the rack is independently sitting on the rail.
Figure 5.13

## Slide 62: Scenario #5
    5.12. Move the crawler back into the car. Hold the lever until you see the “Crawler on Car” label light up (Red circles in Figure 5.14).
Figure 5.14: Crawler Off Car
Figure 5.14: Crawler On Car

## Slide 63: Scenario #5
    5.13. Move the car back into the kiln room to pick up the fully unloading racks.
Unloading Bay
Rack 1
Unloading
Rack 2
Unloading
Loading Bay
Figure 5.15
Rack 1
Loading
Rack 4
Loading

## Slide 64: Scenario #5
    5.14. Move this rack out of the kiln room but this time, drop it off on the loading rail. No need to manually move the crawler this time.
Unloader
Loader
Kiln Room
Figure 5.16
Bessermatic (Loading)
Bessermatic (Unloading)
Rack 3
Mixed
Rack 1
Unloading
New Loading Rack
Car
Auxiliary

## Slide 65: Scenario #5
    5.15. To reduce down-time, collect the loading product and put it in the same bay where all the other loading products have been placed.
Unloader
Loader
Kiln Room
Figure 5.17
Rack 3
Mixed
Car
New Loading Rack
Bessermatic (Loading)
Bessermatic (Unloading)
Auxiliary

## Slide 66: Scenario #5
    5.16. Once that rack has been dropped off, collect the last solid unloading product and put it on the loader rail similarly to step 5.14 (Red circle in Figure 5.18).
Unloader
Loader
Kiln Room
Figure 5.18
Rack 3
Mixed
Rack 2
Unloading
New Loading Rack
Car
Bessermatic (Loading)
Bessermatic (Unloading)
Auxiliary

## Slide 67: Scenario #5
5.17. Pick up the mixed rack from the storage rail and place it on the Unloading rail.
Unloader
Loader
Kiln Room
Figure 5.19
Rack 3
Mixed
Car
Bessermatic (Loading)
Bessermatic (Unloading)
Auxiliary

## Slide 68: Scenario #5
    5.18. While the crawler is dropping off the final rack, go to the “Program Car” page (Red circle in Figure 5.20).
Figure 5.20

## Slide 69: Scenario #6
    5.19. Press on the blue box to the right of the “Location” label until the box says, “Car at Loader” (Yellow circle in Figure 5.21).
Figure 5.21

## Slide 70: Scenario #5
5.20. Flip the control switch back to “Auto” and press the “Auto Pump Start” button (Purple circle in Figure 5.22).
Figure 5.22

## Slide 71: Scenario #5
5.21. Go to the kiln door control panel. Flip the control switch to “Auto” and press the “Auto Start” button (Red circle in Figure 5.23).
Figure 5.23

## Slide 72: Scenario #6
6.1. Wait until the crawler has loaded its first rack onto the new loading bay and has just retrieved its unloading rack. Flip the car control switch to the “Hand” position (Green circle in Figure 6.2).
Figure 6.2
Unloading Bay
Loading Bay
Figure 6.1
Rack 1
Unloading
Rack 2
Unloading
Rack 3
Unloading
Rack 1
Loading
Rack 4
Loading

## Slide 73: Scenario #6
6.2. Use the lever on the second row to move the car to the “reverse” position (Red circle in Figure 6.3). You can press the “Manual Accel” button (Pink circle in Figure 6.3) to speed the car up.
Figure 6.3

## Slide 74: Scenario #6
6.3. hold the “Reverse” lever from step 6.2 until the “Car Centered Left” button lights up (Figure 6.4).
Figure 6.4: off
Figure 6.4: on

## Slide 75: Scenario #6
6.4. Flip the “Left Raillocks” switch to the “Lock” position (Purple arrow in Figure 6.5) and hold it at that position until you see the “Left Locks Locked” box (Red circles in Figure 6.6).
Figure 6.6: Crawler Off Car
Figure 6.6: Crawler On Car
Figure 6.5

## Slide 76: Scenario #6
6.5. Figure 6.7 is what the loading bay should now look like.
Loading Bay
Unloading Bay
Figure 6.7
Rack 1
Unloading
Rack 2
Unloading
Rack 3
Unloading
Rack 1
Loading
Rack 4
Loading

## Slide 77: Scenario #6
6.6. Once the crawler comes back to the car, unlock the raillocks (Purple circle in Figure 6.8), and move the car forward back to the unloading bay. Lock the left raillocks again, making the crawler unload the next rack.
Figure 6.8

## Slide 78: Scenario #6
    6.7. While the crawler is dropping off the final rack, go to the “Program Car” page (Red circle in Figure 6.9).
Figure 6.9

## Slide 79: Scenario #6
    6.8. Press on the blue box to the right of the “Location” label until the box says, “Car at Loader” (Yellow circle in Figure 6.10).
Figure 6.10

## Slide 80: Scenario #6
6.9. Flip the Control switch back to the “Auto” position. Hit the “Pump Auto Start” button (Purple circle in Figure 6.11).
Figure 6.11

## Slide 81: Scenario #6
6.10. Go to the kiln door control panel. Flip the control switch to “Auto” and press the “Auto Start” button (Red circle in Figure 6.12).
Figure 6.12

## Slide 82: Scenario #7
    7.1. Wait until the crawler has loaded its first rack onto the new loading bay and has just retrieved its unloading rack. Flip the car control switch to the “Hand” position (Green circle in Figure 7.2).
Figure 7.2
Loading Bay
Figure 7.1
Rack 1
Loading
Unloading Bay
Rack 1
Unloading
Rack 2
Unloading
Rack 3
Unloading
Rack 4
Mixed

## Slide 83: Scenario #7
    7.2. Use the lever on the second row to move the car to the “reverse” position (Red circle in Figure 7.3). You can press the “Manual Accel” button (Pink circle in Figure 7.3) to speed the car up.
Figure 7.3

## Slide 84: Scenario #7
    7.3. hold the “Reverse” lever from step 7.2 until the car is out of the kiln room and at the furthest rail from the door (Red circle in Figure 7.4). Stop moving the car when the “Car Centered Right” button lights up in this area (Figure 7.5).
Figure 7.5: off
Figure 7.5: on
Unloader
Loader
Kiln Room
Figure 7.4
Bessermatic (Loading)
Bessermatic (Unloading)
Auxiliary

## Slide 85: Scenario #7
    7.4. Before you unlock the rail, flip the “Manual Crawler Auto” switch to the “Crawler” position (Red circle in Figure 7.6).
Figure 7.6

## Slide 86: Scenario #7
    7.5. Flip the “Right Raillocks” switch to the “Lock” position (Purple arrow in Figure 7.7) and hold it at that position until you see the “Right Locks Locked” box (Red circle in Figure 7.8).
Figure 7.7
Figure 7.8

## Slide 87: Scenario #7
    7.6. At this time, move and hold the “Crawler” lever to the “Right” position (Red circle in Figure 7.9) until the entire rack is on the storage railway.
Figure 7.9

## Slide 88: Scenario #7
    7.7. Move and hold the “Crawler Elevator” lever to the “Down” position (Red circle in Figure 7.10) until the rack is independently sitting on the rail.
Figure 7.10

## Slide 89: Scenario #7
    7.8. Move the crawler back into the car. Hold the lever until you see the “Crawler on Car” label light up (Red circles in Figure 7.11).
Figure 7.11: Crawler Off Car
Figure 7.11: Crawler On Car

## Slide 90: Scenario #7
    7.9. Once the crawler comes back to the car, unlock the raillocks (Purple arrow in Figure 7.12).
Figure 7.12

## Slide 91: Scenario #7
    7.10. Take the car to the “Loader” rail and lock the right raillocks.
Unloader
Loader
Kiln Room
Figure 7.13
Rack 4
Mixed
New Loading Rack
Car
Bessermatic (Loading)
Bessermatic (Unloading)
Auxiliary

## Slide 92: Scenario #7
    7.11. While the car is collecting the loading rack, Press the “Program Car” button (Red circle in Figure 7.14).
Figure 7.14

## Slide 93: Scenario #7
    7.12. Press on the blue box to the right of the “Location” label until you see “Car at loader” (Yellow circle in Figure 7.15).
Figure 7.15

## Slide 94: Scenario #7
7.13. Flip the control switch back to “Auto” and press the “Auto Pump Start” button (Purple circle in Figure 7.16).
Figure 7.16

## Slide 95: Scenario #7
    7.14. Wait until all three loading racks have been dropped off at the loader. Follow the car into the kiln room as it takes its loading rack into its proper bay.
Unloader
Loader
Kiln Room
Figure 7.17
Rack 4
Mixed
Rack 3
Unloading
New Loading Rack
Car
Bessermatic (Loading)
Bessermatic (Unloading)
Auxiliary

## Slide 96: Scenario #7
7.15. Once the loading rack has been dropped off, set it back to manual, move the car back to where the mixed-product rack is, and drop it off in the unloader rail.
7.16. Repeat 7.10-7.13.
Unloader
Loader
Kiln Room
Figure 7.18
Bessermatic (Loading)
Bessermatic (Unloading)
Car
Rack 4
Mixed
Auxiliary

## Slide 97
7.17. Go to the kiln door control panel. Flip the control switch to “Auto” and press the “Auto Start” button (Red button in Figure 7.19.
Figure 7.19