## Slide 1: Start-up
6.25.24 version 1.0

## Slide 2
Assumptions and Prerequisite Skills
  The computer is on and IntelliBatch 3.0 is open
  The proper closing procedures were completed the night before
  The power switch is on (HMI screen is on)
Supplies Needed
  Standard PPE Equipment
  Mallet

## Slide 3: Procedure
1. Turn on the lights by door C (Figure 1)
Figure 1

## Slide 4: Procedure
2. To the left of the kiln room door, you will find the air compressor. Push the green button, and check to see if a green checkmark lights up (Figure 2)
Figure 2

## Slide 5: Procedure
3. Right by the air compressor, you will find a door that says “Vapor Generator”. Enter that room and check if the power light (green light) is on. If it isn’t twist and pull out the emergency stop button and press the “reset” button (Figure 3A).
4. Click on the “Run Screen” button. Make sure both rows read “Running” (Figure 3B).
Figure 3A
Figure 3B Running
Figure 3C Not Running

## Slide 6: Procedure
5. If the alarm screen for the generator is showing: Press the “ACK Alarm” to acknowledge the alarm, press “Close” and then press “Reset” (Figure 4)
Figure 4

## Slide 7: Procedure
  Proceed to the car/platform. For the car, press the “CRM reset” button, followed by the “Pump Start” button, and then the “Auto Start” button (Figure 5A)
  For the crawler, press the “CRM Reset/Pump Start” button, followed by the “Auto Start” button (Figure 5B)
Figure 5A Should look like this
Figure 5B. Should look like this

## Slide 8: Procedure
  8. Report to the Bessermatic monitor. Twist and pull out the emergency stop button and press the “CRM Reset” button (Figure 6)
Figure 6

## Slide 9: Procedure
  9. Proceed to the Besser HMI. Twist and pull out the emergency stop button and press the “CRM reset" button (Yellow arrow in Figure 7), followed by the “Pump Start Auto” button (Red arrow in Figure 7)
Figure 7

## Slide 10: Procedure
    10. Go to the Depalleter. Twist and pull the out the emergency stop button and press the “master start/auto enable” button (Red arrow Figure 8)
Figure 8

## Slide 11: Procedure
    11. Proceed to the cuber. Twist and pull out the emergency stop button and press the “Master Start/Auto Enable” button (Red arrow in Figure 9)
Figure 9

## Slide 12: Procedure
    12. Go up the first flight of steps and walk straight ahead. Pull up on the disconnect handle (Yellow arrow in Figure 10). Be sure to push up with force
Figure 10. Should look like this

## Slide 13: Procedure
    13. Twist and pull out the emergency stop button and push the “Reset Safety” blue button (Red arrow in Figure 11)
Figure 11

## Slide 14: Procedure
    14. Press the “Hydraulic Power On” button (Yellow arrow in Figure 12)
    15. Wait about 2 minutes and then hold the switch to the close position (Red arrow in Figure 12) on the “Mixer door 2 open/close” switch until the door/gate is fully closed
Figure 12

## Slide 15: Procedure
    16. Turn the Local/Remote switch to remote (Yellow arrow in Figure 13)
Figure 13

## Slide 16: Procedure
    17. Set scaling to manual on the “Main View” page of IntelliBatch (Figure 14)
Figure 14

## Slide 17: Procedure
    18. Find the Aggregate Weighbelt icon on the top-right side of the page. Click on the orange triangle in the bottom right corner and click “Run” under reverse. This dumps out any potential debris that hardened up overnight (Yellow circle in Figure 15)
Figure 15. Notice how the belt is already running in reverse. The “Run” button would be under the Jog button

## Slide 18: Procedure
    19. Go to the mud hopper. Take out the side screw and lift open the gate flap to break apart any debris that may have stuck overnight (Figure 16A and Figure 16B). Also be sure to remove any stuck debris after the mud hopper as well (Figure 16C). Lastly, remove any debris that may be stuck to the gate in the Machine belt (Figure 16D)
Figure 16A
Figure 16B
Figure 16C
Figure 16D

## Slide 19: Procedure
    20. Go back to the computer. Set Mud Area to manual and run the Mud Hopper 2 belt by clicking run under the reverse tab (Blue circle in Figure 17). All loose debris will now be in the waste hopper
Figure 17

## Slide 20: Procedure
    21. Click on the value in the Mud Hopper and select “Zero Scale”. This will remove any inaccurate weight measurements on the hopper (Blue circle in Figure 18)
Figure 18

## Slide 21: Procedure
    22. For any debris that fell off the mud hopper belt, as well as the debris knocked off from Figure 3D, set the machine belt to reverse. This debris will now be on the floor (Figure 19)
Figure 19

## Slide 22: Procedure
    23. Go to the Mud hopper gate and put the bolt back on (Blue circle in Figure 20). NOTE: make sure the mud hopper belt is turned off at this time.
Figure 20

## Slide 23: Procedure
    24. Go back to the computer and set mixing to manual (Figure 21)
Figure 21

## Slide 24: Procedure
    25. Find the mixer tab, and turn it on by clicking on the orange tringle in the bottom right corner of the icon and holding the start button until you hear the mixer start-up (Blue circle in Figure 22)
Figure 22

## Slide 25: Procedure
    26. Click on the button that says “Empty” at the bottom of the screen (Red circle in Figure 23)
Figure 23

## Slide 26: Procedure
    27. Click on the “Products” Button (Blue circle in Figure 24)
Figure 24

## Slide 27: Procedure
    28. At this point, the “Batch To Block Machine” button will now be available to click on (purple circle in Figure 25)
Figure 25

## Slide 28: Procedure
    29. Check and verify that all of the materials are what you wish to produce your first batch with (Red square in Figure 26). If it isn’t, go back and select/deselect any desired bins/silos (See SOPs Selecting/Deselecting Cement Silos and/or Selecting/Deselecting Aggregate Bins)
    30. After you are satisfied with all the materials listed in the Ingredient list, Click the “Download” button (blue circle in Figure 26) and click the “Cancel” button (Yellow circle in Figure 26)
Figure 26

## Slide 29: Procedure
    31. Set Scaling, Mixing, Discharging, and Mud Area all to auto (Figure 27)
Figure 27

## Slide 30: Procedure
    32. Click on the “Pause” button (Yellow circle in Figure 28)
Figure 28

## Slide 31: Procedure
33. Proceed to the HMI screen
34. Set the Control switch to the Manual position. Press and hold on the “Drop Head Position” until it stops to ensure there is no friction between the head and the mold

## Slide 32: Procedure
35. Set control to auto, vibrators on, and conveyors on (Figure 29)
Figure 29 Should look like this

## Slide 33: Procedure
36. Make sure you are on the “Run Screen” page of the HMI monitor. On the bottom left corner of the screen there would be a button that says “Run Screen” (Figure 30). If there is a blank space on the bottom left corner of the page, then you are in the correct page
Figure 30. Notice the empty spot on the bottom left corner is where the “Run Screen” button would be

## Slide 34: Procedure
37. Press on the “Hydraulic Flow Valve” button (Figure 31)
Figure 31

## Slide 35: Procedure
38. Hit “Home & Reset”. This will set the mold and receiving pallet to its proper positions (Figure 32)
Figure 32

## Slide 36: Procedure
39. Click on the “Vibration Setup” button on the bottom menu. Set the vibration time to 4.500 seconds (Figure 33)
Figure 33

## Slide 37: Procedure
40. Check to make sure proper head, feedbox, pallet positions and speeds are set up in correspondence with the current mold. These can be checked through the “Head & Pallet Receiver Setup” (Figure 34A), “Feedbox & Cutoff” (Figure 34B), and “Pall. Deliv Pall. Trans Setup” (Figure 34C) buttons, all found in the bottom section of the monitor

## Slide 38: Procedure
40. Press and hold “Jog Feed Belt” until the F.B Laser value is above the “Feed Box Full Amount” value to the left of the buttons. This will give our testing pallet enough material to produce the proper output (Figure 34)
Figure 34: Insufficient
Figure 34: Sufficient

## Slide 39: Procedure
41. Press the “Single Cycle” button (Red circle in Figure 35)
Figure 35

## Slide 40: Procedure
42. Press the “Start Machine Cycle” button underneath the monitor (Yellow circle in Figure 36)
Figure 36

## Slide 41: Procedure
44. Wait for the first pallet to come out. Check block height, perform a swipe test, and observe texture. If the pallet meets acceptable standards, press the “Full Auto” button on the “Run Screen” page (Green circle in Figure 37) and hit the “Start Machine Cycle” button again. Else, start troubleshooting the reason behind the bad pallet (SOP troubleshooting bad pallets)
Figure 37

## Slide 42: Procedure
45. After about 5-10 minutes, turn on the “Auto Feed” button (red circle Figure 38). This mechanic automatically adjusts feed time based on block height. Be sure to check the pallets regularly for consistency in quality
Figure 38